## Before Take-off:

- Instructor Approval?

- Flight plan filed?

- Organize cockpit. (charts, clipboard, etc.)

- Note time off and compute time to first checkpoint.

## Climb:

- Climb check list?

- Establish course and heading.

- Open Flight plan with FSS.

## Cruise:

- Cruise Checklist?

- Reset DG every 15 minutes

- Note Checkpoints and update NavLog.

- Always know where you will land if the engine fails.  Check the engine gauges frequently.

- Tune in ATIS then approach (if applicable) when 20nm out.

- Tune in Tower, FSS, Unicom, or CTAF when 10nm out.

## Descent:

- Descent Check List?

- Before Landing Checklist?

- If descending into destination, close flight plan with FSS.

## After Landing:

- Contact ground control when told to do so by the tower. (if appropriate)

- After landing checklist?

- Close flight plan?

## Diversion to an Alternate Airport:

- Figure out where you are and note time.

- Find suitable alternate, turn towards it and change altitude as necessary.

- Figure distance, heading and time to alternate.  MAKE SURE YOU HAVE ENOUGH FUEL!

- Call FSS and amend your flight plan.

- Find out all you can about alternate airport (AFD & Wx)

## Lost Procedures:

- Reset DG with compass!

- Turn back to your original heading and try to match landmarks you see to sectional.

- Climb:  You will see and receive radio better.

- Tune in nearest VOR and identify it with morse code.  (Code shown on chart)

- Center the needle with a TO indication and fly towards the station.

- You should be able to get back on course from the VOR.

IF Still Lost:

- Check fule status and tell FSS/ATC that you are lost (Use 121.5 if urgent)

- They will give you a transponder number and a frequency for Center.

- Center will give you radar vector heading.

If unable to maintain VFR on vector heading, tell Center!

## VFR Lost Communications Procedures:

- Check volume and squelch controls!

- Try other frequencies: they might still work

- If necessary: Squawk 7600 (Lost Comm. Transponder code.

### Evaluate your need for ATC assistance before squawking 7600

- If nearby VOR is voice capable, listen for ATC on the VOR frequency.

- If you are landing at a tower airportL

  - Remain clear of class D airspace until direction of traffic flow is noted.

  - Join the traffic pattern and maintain visual contact with the tower.

  - Watch for light gun signals.  See below:

| Color Steady Green Flashing Green Steady Red Flashing Red Flashing White Red and Green | On Ground: Cleared for takeoff Cleared to taxi Stop Taxi clear of runway Return to starting point Use extreme caution | In the Air: Cleared to land Return for landing Continue circling Do not land; airport unsafe N/A Use extreme caution |
| --- | --- | --- |

  - Acknowledge by rocking your wings (day) or flashing your lights (night)

## Enroute Flight Advisory Service:

##### Getting Updated Weather

- Call “xxx Flight watch”

  - On initial call, tell them N# and the name of nearest VOR

- You can get enroute weather destination reports and forecasts or make pilot reports:

  - To make a Pirep report as much of the following as you can:

    - Report Type……….Routine or Urgent

    - Location……………in relation to VOR

    - Time……………….Zulu

    - Altitude…………….essential for turbulence or icing reports

    - Type of aircraft…….essential for turbulence or icing reports

    - Sky cover…………..Cloud height and coverage (SCT, BKN, or OVC)

    - Weather…………….Visibility, precip, restrictions to vis, etc.

    - Temperature………..in degrees Celsius

    - Wind……………….direction and Magnitude

    - Turbulence…………intensity and duration

    - Icing………………..type ice and rate of accumulation (light moderate, severe)

    - Remarks……………anything not included above or clarification of above items

## Position Reports

Make to nearest FSS as follows:

  - N#

  - Position

  - Time

  - altitude

  - type Flight Plan

  - ETA and Name of next reporting point

  - Name only of succeeding reporting point

  - Remarks